## Slide 1: Efficient Synthetic Traffic Models for Large, Complex SoCs
Jieming Yin, Onur Kayiran, Matthew Poremba, Natalie E. Jerger, Gabriel H. Loh
3/14/2016

## Slide 2: Modeling Traffic for Complex SoCs
CPU
LLC
CPU
CPU
LLC
LLC
GPU
GPU
GPU
GPU
CPU
CPU
CPU
CPU
GPU
GPU
GPU
GPU
LLC
LLC
GPU
GPU
GPU
GPU
LLC
LLC
GPU
GPU
GPU
GPU
GPU
GPU
GPU
GPU
HBM
HBM
How can we efficiently model on-chip communication for future large, complex SoCs?

## Slide 3: Executive Summary
 | Execution-driven simulation | Synthetic traffic | APU-SynFull
Accuracy |  |  | 
Speed |  |  | 
Scalability |  |  | 
Interconnect Simulation For SoCs

## Slide 4: Background on SynFull Methodology
Uses clustering to find a few representative macrophases of execution
  Based on network traffic
Badr et al., ISCA 2014
a macrophase

## Slide 5: Background on SynFull Methodology
Uses clustering to find a few representative macrophases of execution
  Based on network traffic
Uses clustering to capture fine-grain details in a macrophase by identifying microphases
Transitions from one phase to another using Markov chains
  Similar approach for microphases
Badr et al., ISCA 2014
CPU
phase
GPU phase
0.500
0.500
0.125
0.875
a macrophase
a microphase

## Slide 6: Background on SynFull Methodology
Badr et al., ISCA 2014
Cache
LLC
Cache
Cache
Cache
LLC
LLC
LLC
Dir
Dir
Dir
Dir
Initiating message:
application property
Reactive messages:
depend on coherence protocol
Which cache injects the packet?
Chart: Source Node IDs
 | 0.028958 | 0.023166 | 0.025097 | 0.03668 | 0.023166 | 0.040541 | 0.028958 | 0.030888 | 0.034749 | 0.025097 | 0.021236 | 0.03861 | 0.034749 | 0.030888 | 0.027027 | 0.027027 | 0.028958 | 0.03668 | 0.034749 | 0.030888 | 0.03861 | 0.040541 | 0.028958 | 0.023166 | 0.027027 | 0.034749 | 0.03668 | 0.034749 | 0.032819 | 0.03861 | 0.034749 | 0.021236
What is the destination for a given source node?
Chart: Destination Node IDs
 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.14953 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.14953 | 0 | 0 | 0 | 0 | 0 | 0 | 0 | 0.18692 | 0.037383 | 0.037383 | 0.046729 | 0.056075 | 0.028037 | 0.065421 | 0.018692 | 0.2243
Traffic injection amount for each microphase?
Chart: Number of Injections in a Microphase
| 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
 | 0.033149 | 0.038674 | 0.038674 | 0.022099 | 0.044199 | 0.082873 | 0.033149 | 0.044199 | 0.044199 | 0.038674 | 0.022099 | 0.049724 | 0.027624 | 0.027624 | 0.027624 | 0.044199 | 0.027624 | 0.027624 | 0.066298 | 0.066298
…
Generate random numbers from the PDFs derived from application trace

## Slide 7: The Need for an Enhanced SynFull
Summary
Probabilistic models are not always effective in capturing different GPU and CPU phase behaviors
Network traffic is sensitive to phase length selection in APUs
Injection model is not effective in capturing bursty traffic patterns
Not scalable for large systems – requires execution-driven simulation for network traces
Request latencies can be more accurate by introducing a memory latency model

## Slide 8: The Need for an Enhanced SynFull
Significantly different traffic patterns between CPU and GPU phases
Phase transition based on Markov probabilities might lead to too much or not enough traffic
1 - APU Workload Phase Behavior
Chart: Time
Injection rate
Real application behavior: SynFull behavior:
Chart: Time
Different traffic behavior depending on simulation cycles
CPU phase
GPU phase

## Slide 9: Our Methodology: APU-SynFull
Solution: We replay the macrophases in the same order as in the application trace
  More realistic network traffic behavior
  Accurate ratio of CPU and GPU traffic
Disadvantage: No simulation speedup benefits as in the Markov-based phase transition model
Solution: Finish the execution of a macrophase after executing n microphases
  n is determined during model generation, before the actual simulation
  n guarantees reaching the Markov steady-state with m% error (2%) for all macrophases
1 - Deterministic Macrophase Replay

## Slide 10: Our Methodology: APU-SynFull
1 - Deterministic Macrophase Replay - Example
Time
Injection rate
Macrophase length = 5M cycles
Microphase length = 250 cycles
Reaches steady state after 2K microphases
Reaches steady state after 4K microphases
Execute 4K microphases per macrophase:
Simulation speedup = 5M / (4K * 250) = 5

## Slide 11: The Need for an Enhanced SynFull
SynFull results are sensitive to macrophase length selection
2 - Sensitivity to Macrophase Length
Periodic injection rate
  ~1M cycles
Chart: Macro-phase length
| 250K | 625K | 750K
GPU_READ | 1.0264 | 0.91645 | 1.0628
GPU_WRITE | 1.0345 | 0.91969 | 1.05
Can we auto-detect the period for such applications?

## Slide 12: Our Methodology: APU-SynFull
FFT-based approach
  Finds a good macrophase length for applications with periodic injection behavior
Frequency component with the highest FFT coefficient gives the period
  If the period is too long, it can be divided by a factor to make clustering time reasonable
2 - Spectral Analysis for Interval Selection

## Slide 13: The Need for an Enhanced SynFull
3 - Capturing Bursts – temporal Bursts
Chart: Inter-arrival Time (Cycles)
Packets are injected close in time:
high temporal bursts
SynFull injects uniformly over time:
does not model temporal bursts

## Slide 14: The Need for an Enhanced SynFull
3 - Capturing Bursts – Spatial Bursts
Chart: GPU L1Cache nodes
 | 0.029503 | 0.029503 | 0.031056 | 0.032609 | 0.032609 | 0.032609 | 0.032609 | 0.029503 | 0.029503 | 0.032609 | 0.029503 | 0.031056 | 0.032609 | 0.032609 | 0.032609 | 0.029503 | 0.032609 | 0.032609 | 0.031056 | 0.029503 | 0.031056 | 0.032609 | 0.029503 | 0.031056 | 0.031056 | 0.029503 | 0.031056 | 0.032609 | 0.032609 | 0.031056 | 0.029503 | 0.032609
Chart: GPU L1Cache nodes
 | 0 | 0 | 0 | 0 | 0.097674 | 0.088372 | 0.023256 | 0.027907 | 0 | 0 | 0.0093023 | 0.088372 | 0.074419 | 0.065116 | 0 | 0.0046512 | 0.0093023 | 0.023256 | 0 | 0 | 0 | 0 | 0.093023 | 0.060465 | 0.065116 | 0.046512 | 0.013953 | 0.018605 | 0.027907 | 0.04186 | 0.051163 | 0.069767
Each node injects similar amount of traffic in a large window (500K cycles / macrophase)
Nodes inject significantly different amounts of traffic in a smaller window (250 cycles / microphase)
  SynFull doesn’t model spatial bursts

## Slide 15: Our Methodology: APU-SynFull
3 – Capturing Bursts – Temporal Bursts
Time
Number of packets
1 2 3 4 5 6 7 8 9
Probability | Inter-arrival time | Number of packets
60% | 1 | 2
20% | 4 | 4
20% | 2 | 1
Create a PDF of packet inter-arrival times and bursts based on the application network trace
Generate a random pair of inter-arrival time and packet injections from the PDF

## Slide 16: Our Methodology: APU-SynFull
3 – Capturing Bursts – Spatial Bursts
Create a PDF of number of source nodes that can inject packets in a microphase based on application trace
Create a PDF of number of source-destination pairs that packets flow between in a microphase based on application trace
Generate random source and destination node IDs where traffic is observed in a microphase

## Slide 17: The Need for an Enhanced SynFull
We can simulate
4 - Scaling to Larger Systems
We want to simulate
Compute resources are limited
Long time to simulate
Not enough workloads available
How can we create larger synthetic workloads that look like the real workload?

## Slide 18: Our Methodology: APU-SynFull
Spatial Distribution
  Probability of
    Source node sending a message, and
    Destination node receiving a message
4 - Trace Extrapolation
8-node
Traffic Extrapolation
Spatial
Temporal
128-node
Model
File
16-node
32-node
64-node
128-node
Collected Trace
Projected Trace
Temporal Distribution
  Combination of
    On-off model
    Stochastic injection rate
?
16-node
8-node
64-node
32-node
128-node

## Slide 19: The Need for an Enhanced SynFull
No addresses in SynFull → Constant latency memory model must be used
More complicated than using traffic pattern to specify destination memory
  Need row buffer hit rate for accuracy
  Column address also matters - Read from write queue
How are phase addresses represented compactly / clustered with other phases?
  E.g., Stride Access vs. Pointer chasing
5 - Memory Latency Model
Chart: Bank
Chart: Bank
Chart: Bank
≈
≠
Constant latency model error: 25%-75%

## Slide 20: Our Methodology: APU-SynFull
How are phase addresses represented?
  Bank destination distribution
  Transition Matrix = P(BankN|BankM)
  Bank hit rates
How are phase addresses clustered?
  Reduce dimensionality
    Bank distribution → Large magnitudes in FFT
    Transition Vector → P(Consecutive Banks)
    Bank hit rates → Per-channel hit rates
  Standard clustering methods afterward
Replay by reversing above process
5 - Memory Latency Model
Input
Distribution
Transition Matrix
Hit Rate Statistics
Synthetic Model
FFT
Clustering

## Slide 21: Evaluation
APU with 32 CUs and 1 CPU
2D Mesh network
Gem5 & GPU model
  Collect traces
  Generate APU-SynFull models
Instantiate APU-SynFull nodes to a network simulator (Garnet) to simulate network traffic
Macrophase length: 5M cycles
  Autodetected for periodic applicatons
Microphase length: 250 cycles
In the paper: sensitivity to phase lengths
Baseline & Methodology

## Slide 22: Evaluation
Chart: Percentage error in average network latency
| bitonic | dct | histogram | matrixmul | spmv | comd | backprop | bfs | hotspot | nw | AVG
SynFull | 0.29835 | 0.26204 | 0.20224 | 0.36075 | 0.24824 | 0.13659 | 0.52158 | 0.12723 | 0.51258 | 0.43385 | 0.31035
APU-SynFull | 0.011595 | 0.2154 | 0.15999 | 0.097523 | 0.10715 | 0.035838 | 0.05293 | 0.040472 | 0.23312 | 0.12847 | 0.10825
Network Latency Results
In the paper:
Latency distributions
Distributions of injected message types
Capturing bursts
Macrophase replay
Automated phase length

## Slide 23: Evaluation
Strong Scaling Results
Chart: Distribution of initiating messages
| Scaled | Baseline | Scaled | Baseline | Scaled | Baseline | histogram | matrixmul | bfs
CPU_READ | 66986 | 71991 | 3914 | 136832 | 286154 | 288075
CPU_WRITE | 0 | 0 | 0 | 4735 | 0 | 0
GPU_READ | 42793 | 65648 | 325412 | 2255427 | 723526 | 689803
GPU_WRITE | 349 | 544 | 219452 | 981952 | 269545 | 274430
GPU_L2_EVICT | 0 | 0 | 34805 | 5919 | 0 | 0
Chart: Average network latency
| Scaled | Baseline | Scaled | Baseline | Scaled | Baseline | histogram | matrixmul | bfs
Average network latency | 31.6054 | 29.5577 | 43.0778 | 49.282 | 50.24 | 51.7561
In the paper:
Weak scaling results
Scaled: extrapolated traffic for the 128 CU system
Baseline: execution-driven system with 128 CUs

## Slide 24: Evaluation
Latency error between model and true latency improved by ~37%
  Largest error source from FFT compression
  High burst phases have more error
Hit rate error within 12% of true hit rate
Synthetic approaches are promising! → Avoid constant latency model
Memory Latency Results
Chart: Memory Latency Model Mean Error and Deviation
| bitonic | dct | histogram | matrixmul | spmv | comd | bfs | hotspot | nw | AVG
Fixed Latency | 0.50379 | 0.49154 | 0.57043 | 0.65088 | 0.63765 | 0.55397 | 0.32766 | 0.59073 | 0.5542 | 0.54232
APU-SynFull | 0.52203 | 0.38739 | 0.14566 | 0.44869 | 0.26957 | 0.25087 | 0.29058 | 0.43603 | 0.32978 | 0.34229
Chart: Read Count/Write Count/Hit Rate Error
| bitonic | dct | histogram | matrixmul | spmv | comd | bfs | hotspot | nw | AVG
Read Count Error | 0.28753 | 0.11948 | 0.016868 | 0.08545 | 0.14246 | 0.032805 | 0.13334 | 0.13942 | 0.070446 | 0.1142
Write Count Error | 0.41964 | 0.18902 | 0.025336 | 0.22004 | 0.065052 | 0.067983 | 0.19357 | 0.36035 | 0.11938 | 0.18449
Hit Rate Error | 0.22305 | 0.092016 | 0.030709 | 0.14889 | 0.18903 | 0.05002 | 0.15445 | 0.097964 | 0.096836 | 0.12033

## Slide 25: Conclusions
We identify various challenges in modeling network traffic in SoCs
We propose a methodology for simulating large scale heterogeneous systems
Can explore network and memory designs (faster) with synthetic APU-like workloads, without execution-driven simulators
Captures many different traffic patterns – useful for not only CPU and GPU, but other components
  Accelerators, FPGAs, different IPs

## Slide 26: Thanks!

## Slide 27: Disclaimer & Attribution
The information presented in this document is for informational purposes only and may contain technical inaccuracies, omissions and typographical errors.
The information contained herein is subject to change and may be rendered inaccurate for many reasons, including but not limited to product and roadmap changes, component and motherboard version changes, new model and/or product releases, product differences between differing manufacturers, software changes, BIOS flashes, firmware upgrades, or the like. AMD assumes no obligation to update or otherwise correct or revise this information. However, AMD reserves the right to revise this information and to make changes from time to time to the content hereof without obligation of AMD to notify any person of such revisions or changes.
AMD MAKES NO REPRESENTATIONS OR WARRANTIES WITH RESPECT TO THE CONTENTS HEREOF AND ASSUMES NO RESPONSIBILITY FOR ANY INACCURACIES, ERRORS OR OMISSIONS THAT MAY APPEAR IN THIS INFORMATION.
AMD SPECIFICALLY DISCLAIMS ANY IMPLIED WARRANTIES OF MERCHANTABILITY OR FITNESS FOR ANY PARTICULAR PURPOSE. IN NO EVENT WILL AMD BE LIABLE TO ANY PERSON FOR ANY DIRECT, INDIRECT, SPECIAL OR OTHER CONSEQUENTIAL DAMAGES ARISING FROM THE USE OF ANY INFORMATION CONTAINED HEREIN, EVEN IF AMD IS EXPRESSLY ADVISED OF THE POSSIBILITY OF SUCH DAMAGES.
ATTRIBUTION
© 2013 Advanced Micro Devices, Inc. All rights reserved. AMD, the AMD Arrow logo and combinations thereof are trademarks of Advanced Micro Devices, Inc. in the United States and/or other jurisdictions. SPEC is a registered trademark of the Standard Performance Evaluation Corporation (SPEC). Other names are for informational purposes only and may be trademarks of their respective owners.